## Slide 1: Towards Quantum Information Processing with Femtosecond Laser Pulse Induced Manipulation of Matter
Debabrata Goswami IIT Kanpur, India
Thermal
Optical
MCIT
Swarnajayanti Fellow
Wellcome Trust International Senior Research Fellow
MHRD Virtual Labs
ISRO STC Funds
Funding
A. Nag, S.K.K. Kumar, A.K. De, T. Goswami, I. Bhattacharyya, S. Maurya, A. Kumar, D.K. Das, P. Kumar, D. Roy, D. Das, D. Mondal, K. Makhal, S. Dindha, S.N. Bondhopadhyay, S. Sanghal, R.K. Gupta, Y. Yadav, S. Patel, A. Bose, S. Priyadarshi, S. Chapekar, A. Dutta, V. Singh, N. Gupta, S. Ashtekar, P. Samineni, N. Mutyal, etc.
Students
ISCQI-2016, IoP Bhubaneshwar, Feb. 16, 2016

## Slide 2
Matter under the influence of optical perturbation can behave quite differently – more so when such perturbations are abrupt and extreme. We use femtosecond pulse shaping approaches with femtosecond lasers that are suitably tailored for controlled laser-matter interactions.
Such light-matter interaction can unravel many hitherto unseen phenomena, a few of examples from our recent work encompass: optical microscopy, nano-material manipulation under optical field, nano-scale probe temperature sensor, coherent oscillations from micro-heterogeneity, as well as demonstrating the molecular nature of thermal lens spectroscopy.
Theoretical understanding of these new prospects provides further importance to such ultrashort timescale interactions.
“Characterization & Manipulation at High Spatiotemporal Resolution”

## Slide 3
Intramolecular relaxation occurs on a few-fs time scale, so long pulses excite entire molecule, and the weakest bond breaks, no matter which bond was excited. We need the pulse in femtosecond regime.
Excite one bond
A few fs later, however, the entire molecule is vibrating.
The bond vibrates
Problem of molecular control: Laser Matter Interaction at Individual Pulse Level

## Slide 4: Gas Phase Experimental setup

## Slide 5
Controlling Chemical Dynamics
T. Goswami, D.K. Das and D. Goswami, CPL Cover (2013)

## Slide 6: Single Laser Pulse Interaction
Sample
Pump
Probe
LASER
Condensed Phase: Effect of solvent

## Slide 7
Decay of the transient absorption of IR775 in the binary mixture of MeOH-CHCl3

## Slide 8: Time-resolved pump-probe dynamics of IR775 dye in binary mixture of methanol & chloroform
60% MeOH
80% MeOH
Microheterogeneity

## Slide 9
Microheterogeneity…
S1
S0
Energy
Reaction coordinate (Solvent Coordinate)
IVR
VC
τ1 =100 fs
τ2 ≥350 fs
τ3 ≥280 ps
T1 ≥250fs
T2 ≥280fs
Schematic representation of the excited state dynamics
Measurements
Das, Makhal, Bandyopadhyay, and Goswami, Scientific Reports 4, 6097 (2014)
Simple Model

## Slide 10: Pulse Shaping
Programmable Control over amplitude, phase, frequency and/or inter-pulse separation.
Programmable Fourier Approaches
D. Goswami, Physics Reports
374(6), 385-483 (2003).
Notes: This slide shows the programmability and computer control of the pulse shaping process which will be critical in our experiments.
I developed and constructed such a UTOPS for the first time it as a graduate student and I currently have a modern version of it in my lab now. This is a completely programmable amplified pulse shaper and has a demonstrated operating capability at 20kHz and could in principle be operated up to a MHz. Current repetition restriction in my system is due to my amplified laser system that is optimized for high power wide spectral tunability. Let me show my current laser system.

## Slide 11
Pulse Pair
Pulse Train
High-Repetition Laser Pulse Shaping:
Application to Microscopy
(Tomorrow: Soumendra Bandyopadhyay)
A.K. De, D. Roy, D. Goswami, JBO Lett. (2011)
D. Goswami, D. Das, S.N. Bandyopadhyay, Faraday Dis. (2015)

## Slide 12: Stimulated Emission Depletion (STED) Fluorescence Microscope (Stefan Hell) 2014 Nobel Prize Award Winning Work
Depletion
In Space XY Plane
Our Time Domain Approaches with Pulsed Lasers
Excitation
Time 
Making laser spot size – PSF - smaller by using Depletion effect of fluorophore.
Pulse Train
Pulse Pair
S0
Absorption
Stimulated Emission
Fluorescence
Superresolution

## Slide 13
F
E
M
T
O
S
E
C
O
N
D
P
U
L
S
E
S
C
A
N
N
I
N
G
M
I
C
R
O
S
C
O
P
Y
BACKGROUND: High-rep-rate is critical: Ensures every pixel has pulses available
Exciting Laser Beam
Quenching Laser Beam
Our Pulse-pair Microscopy: Distinct from
STED

## Slide 14
Change in relative intensity of DAPI versus Texas Red
Fluorescence suppression image of Texas Red relative to DAPI (λex = 750 nm)
Excitation & emission of Texas Red and DAPI dyes
Pulse-sequence excitation in fluorescence microscopy
Selective fluorescence suppression by stimulated emission

## Slide 15: Ultrafast pulse-train control in fluorescence laser-scanning microscopy
TexasRed
Selective suppression of fluorescence with time delayed pulses.
Resolution enhancement for overlapping fluorophore Images.
Enhanced spatial resolution with temporal pulses.
A.K. De, D. Roy, D. Goswami, JBO Lett. (2011)

## Slide 16
Axial edge response function
Gaussian fitted derivative of axial edge response function
40X, 1.3 NA objective
60X, 1.42 NA objective
Change in axial resolution as a function of inter pulse delay (R6G in MeOH)

## Slide 17: Axial Resolution versus Inter-pulse separation of DAPI stained BPAE cell

## Slide 18
X
Y


Lateral
Axial
Confocal
MICROSCOPY
RESOLUTION

## Slide 19
SEEING IS …
BELIEVING
WITH SUFFICIENT
RESOLUTION
CHARACTERIZATION

## Slide 20
Shaped RF wave
Acousto-Optic Modulator (TeO2)
Grating 1
Grating 2
Curved Mirror 1
Curved Mirror 2
M
M
M
M
M

## Slide 21
ultrafast thermo-optic manipulations

## Slide 22
Why Bother!?
Rationalizing Scientific Hunger
16
Individual level manipulation
Temperature &/or viscosity effects…
Molecular level information?!
Bulk versus interface…

## Slide 23
Here, ; ; m= n/nm
where, E is electric field of the electromagnetic radiation.
Basic Theory
K. Svoboda and S. M. Block, Annu. Rev. Biophys. Biomol. Struct. 23, 247-285 (1994).
A. Ashkin, Biophys. J. 61, 569-582 (1992).
The force acting along the direction of the incident ray is called Scattering Force
The force acting along the perpendicular direction of the incident beam is called Gradient Force
Light in
Bright ray
Dim ray
Light in
p1
p′1
p2= -Δp
Force
Δp= p′1- p1
p1
p′1
p′1
p′1
p1
p2= -Δp
Force
Δp= p′1- p1
λ
Trapping force in Mie regime (d>>λ):
Z
Y
T2P
TRP
TP
P
RP
f
rap
Φ
FScat
FGrad
Î
Trapping force in Rayleigh regime (d<<λ):
Assuming a steady-state condition, the net radiation force F on the particle-
Here, outwardly directed normal unit vector,
Maxwell's stress tensor.
Trapping for intermediate size regime(d≈λ):
θ
ε

## Slide 24
Pulsed Optical Trap: EXPERIMENTAL SETUP
Two photon
Fluorescence signal
Backscattered signal
Incident laser beam

## Slide 25
Trapping of 4 μm diameter PS microsphere in water with CW laser
Trapping of 4 μm diameter PS microsphere in water with mode – locked laser
When another particle comes when one 4 μm particle is already trapped
Manipulation of trapped of 4 μm diameter PS microsphere in water with CW laser
Trapping of 100 nm diameter Latex microsphere in water with mode – locked laser under bright field
Trapping of multiple 100 nm diameter Latex microsphere in water with mode – locked laser.
Experimental Techniques
Video of Trapping Events

## Slide 27
13 ns
~120fs
Average Power
Time →
t = 0 s
t = 13 ns
t = 0–13 ns
Laser ON Particle Under Trapping Force
Laser OFF Particle Under NO Trapping Force
Laser ON Particle Under Trapping Force
Brownian motion within focal region
V→
V = 0
Radial Axis
← stable trapping →
Potential
Energy (V)
Z Axis
Beam Axis
Radial Axis
Tightly Focused
Gaussian Beam
Shallow Potential Well
(CW Excitation)
Steep Potential Well
(Pulsed Excitation)
Particle
V = 0
Trap center
TEM00 Mode Gaussian Pulse:
Potential Energy U, for Rayleigh Particles:
Stable Trapping Condition:
Effect of Laser Repetition Rate:
t = – 20 fs
t = – 10 fs
t = 0 fs
t = 10 fs
t = 20 fs
τ = 100 fs
Basic Theory for Rayleigh Particles (Dipolar Approximation)
L. Wang, C. Zhao Opt. Express 15 10615 (2007).
L. Wang H. Chai Opt Express 19 14389 (2011).

## Slide 28
force depends on polarizability: e.g., latex nano-particles are hard to trap
high peak power of an ultra-short pulse but ‘Repetition Rate is Critical’
requires high repetition rate of the pulses
(steep potential well)
(pulsed excitation)

## Slide 29
TWO PHOTON FLUORESCENCE
Single-photon Excitation
h
h
Absorbtion
Emission
photon
non-excited
dye molecule
2photon-excited
dye molecule
Two-photon Excitation
h
h*
h*
Absorbtion
Emission

## Slide 30
1)
2)
Trapping of 100 nm Latex Bead
Observed through Two-photon Fluorescence Signal only—calibrated from back-scattering data of 4 & 1 micron
Particle aggregation can also be tagged through this extremely sensitive technique (see case 2)
Simultaneous coupling pulse shaping to this efficient and sensitive ultrafast optical tweezers is possible to let us reach our goal towards spatiotemporal control and spectroscopy
Direct Trapping of Rayleigh or sub-diffraction sized particles (λ >> d)

## Slide 31
Stable trapping of 100 nm latex beads
Trapping of 16 nm Q-dot
Capabilities of Single Beam Femtosecond Optical trap

## Slide 32
4.1 μm
1 μm
τ1 = 5s
τ2 = 270 s
τ1 = 17s
τ2 = 550 s
0.1 μm
0.5 μm
Time (sec.)
τ = 13s
2 μm
Time (sec.)
Time (sec.)
Time (sec.)
Time (sec.)

## Slide 33
Trapped Microsphere Material: Polystyrene Coated with Dye Having λmax of Absorption and Fluorescence at 580 nm and 605 nm Respectively
Diameter of Trapped Microspheres: 1 μm, 2 μm and 4 μm
Bi-exponential Decay in Two Photon Fluorescence Intensity coming from the Microspheres Under Trapped Condition
No Decay Found when Two Photon Fluorescence Collected
while Untrapped
Untrapped
Fluorescence Energy Transfer in Trapped Objects
Trapping of 1 μm, 2 μm and 4 μm Polystyrene Microsphere
D. Roy, D. Mondal, D. Goswami Chem. Phys. Lett. (Cover Article) 621 203 (2015).
4 μm Trapped
τ1 ~ 0.53 s, τ2 ~ 15.4 s
2 μm Trapped
τ1 ~ 0.36 s, τ2 ~ 17.2 s
1 μm Trapped
τ1 ~ 4.20 s, τ2 ~37.6 s

## Slide 34
No Decay in Back Scattered Signal while Trapped: Trapped Microspheres Do Not Gradually Move Out of the Trap
Excitation and Two Photon Fluorescence Spectra Remain Same for the Trapped Microspheres: Dye Characteristics Remain Same
Area Under the Curve for Two Photon Fluorescence Spectra Increases with Size: Amount of Fluorescence Increases with Size: Also Evident from the TPF versus Time Plot Under Trapped Condition
Temperature Rise During Trapping Very Small (< 1°C)
Fluorescence Energy Transfer in Trapped Objects
Back Scattered Signal and Dye Characteristics
A. K. De, D. Roy, D. Goswami Curr. Science 101 935 (2011).
A. K. De, D. Goswami J. Fluorescence 19 381 (2009).

## Slide 35
r
z
Stokes’ Shift of the Coated Dye is Small (~25 nm): Fluorescence Reabsorption can Occur
Wavelength of Laser: 780 nm
NA of the Objective: 1.4
Focal Spot Size = (1.22×λ)/NA ~ 700 nm
Partial Illumination of the Trapped Microspheres occur: Fluorescence Resonance Energy Transfer occurs between the Dyes in the Illuminated Area to those in the Non‒illuminated Area
Amount of Non‒illuminated Area Increase with Increase in the Diameter of the Trapped Microspheres
1 μm
2 μm
4 μm
Fluorescence Energy Transfer in Trapped Objects
Partial Illumination of 1 μm, 2 μm and 4 μm Polystyrene Microsphere
D. Roy, D. Mondal, D. Goswami Chem. Phys. Lett.(Cover Article) 621 203 (2015).

## Slide 37
Dimer formation: Simultaneously Trapped Two Nanospheres: Two possible orientations
Single Nanosphere Trapping
Trimer formation: Simultaneously Trapped Three Nanospheres: Two of the many possibilities
Tetramer formation: Simultaneously Trapped Four Nanospheres:
Two of the several possible orientations
Multi–Particle trapping: Possibilities of Aggregation

## Slide 38
Y. Cao et. al., Optics Communications 311, 332–337 (2013)

## Slide 39
Particles Trapped: Dye Coated Microsphere with Diameter 0.5 μm
Particle Diameter < Focal Spot Size (700 nm): No Decay in TPF for Trapped Single Microsphere
Usage of High NA objective: Very High Optical Gradient Force
Small Size Particle and High Optical Gradient Force: Multi‒particle Trapping
Up to 4 Particle Trapping Observed
Laser Polarization: Horizontal
No Decay in TPF for Two Particle Trapping: Particles are Oriented along z‒axis, NOT radially: Earlier Reports
1 Particle Trapping
2 Particles Trapping
Probing the Structure and Dynamics of Optically Bound Clusters
Trapping using Horizontally Polarized Light
M. Li , J. Arlt Opt. Commun. 281 135 (2008).
S. Xu, Z. Sun J. Chem. Phys. 126 144903 (2007).
S. K. Mohanty, J. T. Andrews, P. K. Gupta Opt. Express 12 2746 (2004).
D. Roy, D. Mondal, D. Goswami Chem. Phys. Lett. (Cover) 621 203 (2015).

## Slide 40
3 or more Trapped Particles: Cluster Dimension > Focal Size: TPF Decay
TPF Decay: Single Exponential
τ3 Particle ~ 5.1 s, τ4 Particle ~ 7.3 s: 4 Particle Cluster has Less Non‒illuminated Area
Three Particle Trapping:
Optical Gradient Force Controlled Cluster: Configurations (a), (b) not possible
Most Favored Configuration: (c)
Cluster Structure: Combination of Configurations (c), (d), (e)
Four Particle Trapping:
Possible Configurations: Pyramidal
(a)
(b)
(c)
(d)
(e)
Favored
Structure
Probing the Structure and Dynamics of Optically Bound Clusters
Trapping using Horizontally Polarized Light: Various Cluster Configurations
Unlikely
Unlikely
D. Roy, D. Mondal, D. Goswami Sci. Reports (submitted)

## Slide 41
Particle Size 0.5 micron : Circular Polarization
No decay in TPF intensity of single particle trapping
TPF intensity decay in two particle trapping with τ=23.5 sec, three particle trapping with τ=0.5 sec and in four particle trapping with τ=8.4 sec
In Circularly polarized beam, due to rotation of cluster, some area of the cluster remains outside the illuminated zone
Long spikes arises due to biased diffusion of large sized cluster through the focal region
Multi – Particle trapping
τ=0.5
τ=8.4
τ = decay constant using single exponential decay
τ=23.5

## Slide 42
Laser Polarization: Circular
Long Spikes: Biased Diffusion of Large Clusters
Single Particle Trap: No TPF Decay
Clusters: Shape‒birefringence: Rotate
2 or more Trapped Particles: Cluster Dimension > Focal Size: TPF Decay
TPF Decay: Single Exponential
τ2 Particle ~ 23.5 s, τ3 Particle ~ 0.5 s, τ4 Particle ~ 8.4 s
3 particle Rotating Cluster Structure: Combination of Configurations
Probing the Structure and Dynamics of Optically Bound Clusters
Trapping using Circularly Polarized Light
D. Roy, D. Mondal, D. Goswami CPL (Cover) 621 203 (2015).
D. Roy, D. Mondal, D. Goswami Sci. Reports (submitted)

## Slide 43
Small Rayleigh Particles Can be Stably Trapped with High Repetition Rate Femtosecond Laser Pulses at a Much Lower Average Power
For Large Cluster of the Rayleigh Particles, Decay in Two Photon Fluorescence is Observed
Fluorescence Energy Transfer Occurs Between the Dye Molecules Present on the Illuminated Surface to the Non‒illuminated Surface of the Trapped Objects
The Structure and Dynamics of the Optically Bound Clusters are Probed using Fluorescence Energy Transfer Process
Two Photon Fluorescence is Not Only a Good Background Free Detection Scheme but Also Probes the Structure and Dynamics of Optically Bound Clusters and Calibrate Optical Tweezer
Present Status…

## Slide 44: Problem Statement
Materials under the influence of
thermal perturbation can
behave quite differently
Certain such effects can be measured
      using thermal lens spectroscopy

## Slide 45
Why Thermal Lens Spectroscopy?
Thermal lens spectrometry (TLS) is 100 to 1000 times more sensitive than the traditional absorption spectrophotometry.
TLS has been employed for the detection of trace amounts of heavy metal ion such as lanthanides, lead (II), toxic chemical compound etc.
TLS has been employed single molecule detection and its characterization.
Study of higher overtones and combination bands.
Study of photochemical reactions.
Accurate quantification of the fluorescence quantum yield without reference sample.
R. Saavedra, C. Soto, R. Gómez, A. Muñoz, Microchemical Journal, 110, 308, 2013.
D. Boyer, P. Tamarat, A. Maali, B. Lounis, M. Orrit, Science , 297, 1160, 2002.
J. G. Navea, A. Lopez-Calvo, C. E. Manzanares, J. Phys. Chem. A, 110, 1594, 2006.
N. G. C. Astrath, F. B. G. Astrath, J. Shen, J. Zhou, K. H. Michaelian, C. Fairbridge, L. C. Malacarne, P. R. B. Pedreira, P. A. Santoro, M. L. Baesso, App. Phys. Lett, 95, 191902, 2009.
A. Santhi, U. L. Kala, R. J. Nedumpara, A. Kurian, M. R. P. Kurup, P. Radhakrishnan, V. P. N. Nampoori, Appl. Phys. B, 79, 629, 2004.

## Slide 46
hυp
ISC
S1
S0
hυ
1
2
0
3
0
1
2
3
VR
NR
NR
hυf
Jablonski energy diagram
Radiative
Non-Radiative
hυf → Fluorescence
hυp → Phosphorescence
VR → Vibrational relaxation
ISC→ Intersystem crossing
Thermal Lens
Excitation by Electro-magnetic radiation
Creation of spatial Temperature distribution
Change in density
Formation of refractive index gradient
Basic Principle:
Probe Beam
Pump Beam
Thermal lens
Sample cell
Thermal Lens Spectroscopy
Ultra-sensitive
Non-destructive
J. P. Gordon, R. C. C. Leite, R. S. Moore, S. P. S. Porto and J. R. Whinnery, J. Appl. Phys. 36, 3 (1965).
S. E. Bialkowski, Photothermal Spectroscopy Methods for Chemical Analysis (Wiley, New York, 1996).

## Slide 47
Thermal Lens (TL) with Pulse Train
Thermal lens effect due to a Continuous Wave (CW) Laser.
Thermal lens effect due to a single femtosecond pulse is insignificant.
In the case of high repetition rate (HRR) lasers, this transient heating accumulates in the sample and result into a long time TL signal.

## Slide 48
IMRA
Retro
Laser Pulse Characterization
~100fs
~300fs
20ns

## Slide 49
IMRA
DM: Dichroic Mirror
G: Glass Plate
L: Lens
M: Mirror
A: Attenuator
DM
DM
G
M
M
M
M
M
L1
L
L
Iris
L
-
+
Shutter
L
L2
S
S
780nm
1560nm
P. Kumar , S. Dinda, D. Goswami, Phys. Chem. Chem. Phys., 2014, 16, 12291
EXPERIMENTAL
SETUP
A
TL Signal,

## Slide 50
Earlier Thermal Lens Model by Shen et. al.
Heat load
Heat transfer by conduction
Heat transfer by convection
Conduction only model for Low absorbing Sample
Net Heat Change
v =z1/zp,
m = (ωp/ωe)2
Where,
Coupled variable equation:
Not possible to solve analytically
Heat Equation
J. Shen, R. D. Lowe and R. D. Snook, Chem. Phys. 165, 385 (1992).
Shen model of Thermal Lens Study

## Slide 51
Alcohols have a strong absorption band at 1560 nm wavelength: vibrational combination states of “OH” couples with femtosecond laser pulses centered at 1560 nm.
The amplitude of thermal lens signal, S, at various z-positions of the sample at a given time, t, is given as
P. Kumar, S. Dinda, A. Chakraborty, D. Goswami, Phys. Chem. Chem. Phys., 16, 12291, (2014).
Unusual Behavior of TL Signal in Alcohols
Notes: Alcohols have a strong absorption band at 1560 nm wavelength. The vibrational combination states of “OH” group couples with femtosecond laser pulses centered at 1560nm. The absorption spectra of homologous series of primary alcohols is shown in figure.
Methanol has the highest absorption around 1560 nm wavelength compared to the rest of the series. Higher is the absorption of the pump beam, the higher will be thermal lens signal.
The amplitude of thermal lens signal, S, at various z-positions of the sample at a given time, t, is given in equation 4.1. The TL signal for various alcohol is given in the figure. For analysis, we have taken TL signal at the focal point. In spite of the fact that, methanol has the highest absorption of the pump beam, it has lesser TL signal compared to the adjacent member of the series. And propanol has the highest TL signal in the series.

## Slide 52
Another important thermal lens model by Marcano et. al. can also be reduced for the stationary TL form at z = 0 as,
4.9
4.10
Both Shen and Marcano’s models can be related for our particular experiments as:
P. Kumar, S. Dinda, A. Chakraborty, D. Goswami Phys. Chem. Chem. Phys., 16, 12291, (2014).
Unusual Behavior of TL Signal in Alcohols
CH3(CH2)nOH
For primary linear chain aliphatic alcohol series of the form:
Our Experimental data deviates heavily from the existing Thermal Lens (TL) models
Notes: Similarly Marcano et. al. model (eq. 4.8) can also be reduced for the stationary TL form at z = 0 as
So, we can relate both Shen and Marcano’s models for our particular experiments as follows:
The TL signal calculated from these two models is plotted with the experimental TL signal. Either of them, does not explain the behavior of TL signal in a series of alcohols.

## Slide 53: Shen Model versus Experiments
Key reason: Absorbing samples!
&/or High Laser Pulse energy

## Slide 54
Alcohol Series:
High Laser Pulse energy more critical for deviation

## Slide 55
Highly absorbing Sample
(Alcohols)
Shen Model fails!!
Retention of Convective Term
TL Signal fits well!

## Slide 56
Time Resolved Thermal Lens Signal
where, , )exp(-t/td) = θconv exp(-t/td)
Unusual Behavior of TL Signal in Alcohols
P. Kumar, A. Khan, D. Goswami. Chem. Phys. 441, 5 (2014).
Notes: We also measured the time resolved Thermal lens signal of the series at the focal point of the pump beam.
Time resolved TL signal for Methanol and ethanol passes through an inflection point. Similar inflection points were previously found in the case of photochemical reaction. But in our case, no such photochemical reaction is found.
We also compared the time resolved data with the Shen model given in equation 4.6. Which shows a completely mismatched between experimental TL signal and the model signal.
So we looked back at the starting equation of thermal lens model and proposed that for strong absorbing samples, equation 4.3 is to be solved for thermal lens model. However, the equation is not solvable. So we took the full solution as in equation 4.5 and made the appropriate changes in the equation.
On the argument that absorbed energy has two parts: one part of energy is transferred by conduction and the second part of energy is transferred by convection. Similar to thermal conductivity coefficient (k), we define h is the factor which defines the heat convection. With this model equation, we fit the experimental data, we extract important information.

## Slide 57
(a)
H2O
Effect of conduction minimum
High effect of conduction

## Slide 58: Thermal Effect to Tweezers Measure
D. Mondal and D. Goswami, Biomedical Express, 6(9), 3190-3196 (2015)

## Slide 59
Instrumentation
Y
X
X
Y
X = [(V2+V3)-(V1+V4)]/[V1+V2+V3+V4]
Y = [(V1+V2)-(V3+V4)]/[V1+V2+V3+V4]

## Slide 61
Results & Discussions

## Slide 64
1560 nm Power (μW) | Corner Frequency (Hz) | Trap Stiffness (pN/nm) | Temperature Rise (°C)
0 | 131(±4) | 0.0069(±.00021) | 0
100 | 142(±4) | 0.0075(±.00023) | 0.05
210 | 149(±4) | 0.0078(±.00024) | 0.10
350 | 157(±7) | 0.0082(±.00025) | 0.16
420 | 165(±12) | 0.0087(±.00026) | 0.19
540 | 173(±15) | 0.0091(±.00027) | 0.25
680 | 181(±15) | 0.0095(±.00028) | 0.31
800 | 195(± 16) | 0.0102(±.00030) | 0.37

## Slide 65
Plot of Inverse corner frequency (blue square), as well as viscosity for experimental (red circle) and simulated case (black circle) and their respective linear fits; all plotted with respect to 1560 nm femtosecond laser power.

## Slide 66
D. Mondal and D. Goswami, Biomedical Express, 6(9), 3190-3196 (2015)

## Slide 67
Measurement
of Nonlinearities
Coherent Control
Bioimaging
  Multiphoton Imaging
  Optical Tweezers
2-D IR Spectroscopy
Thank You
For more info please visit
http://home.iitk.ac.in/~dgoswami
Questions?
Fin

## Slide 68
Nanophotonics
Coherent Control
Quantum Computing
Nonlinear Spectroscopy
Thermal Lens Microscopy
Femtosecond Pulse Shaping
Optical approaches in biology
Optical coding and transmission
High-finesse sensitive spectroscopy
Spatiotemporal control through laser-matter interaction
Femtosecond Laser Multiphoton Imaging & Optical Tweezers
Selective photo-fragmentation in supersonic molecular beams
Excite one bond
The bond vibrates
Experiments in the World of Femtoseconds
(1 fs = 10-15 s)
FEMTOSCIENCE
Entire molecule vibrates
A few fs later
Research Activities